## Slide 1: Confined Space Regulations
Riverton Case Study

## Slide 2: This is Danny Crump

## Slide 3: Excerpt from Police Report
On 07/21/2009, I was dispatched on an unattended death at 1830 West 11800 South. The call stated there was a male in a water manhole in full arrest.
Unified Fire Heavy Rescue 121, Unified Fire Ladder 120 and South Jordan Police were on scene.
I was informed by Unified Fire that the male inside the manhole was deceased. The deceased male was identified as Danny Crump. I spoke with a male, [Riverton City employee] was on scene and he stated he was the first one there and noticed Danny. [Employee] stated he did not go inside the manhole and called 911. [LUCKILY EMPLOYEE DID’NT ATTEMPT RESCUE]

## Slide 4: Excerpt from Police Report (cont.)
Medical Examiner’s opinion: Danny Crump died as the result of asphyxia due to suffocation.
This results when there is lower than normal amounts of oxygen in the respired air available. This can be the result of consumption of the oxygen by natural processes or by replacement of the oxygen by other gases such as methane, carbon dioxide or nitrogen.

## Slide 5: Citation
Citation resulted in 9 separate violations
Permanent record of what happened, found on OSHA website:
Inspection Detail | Occupational Safety and Health Administration osha.gov

## Slide 6: What is a confined space? 29 CFR 1910.146(b)
(1) Is large enough and so configured that an employee can bodily enter and perform assigned work;
(2) Has limited or restricted means for entry or exit (for example, tanks, vessels, silos, storage bins, hoppers, vaults, and pits are spaces that may have limited means of entry);
(3) Is not designed for continuous employee occupancy.

## Slide 7: Construction v. Maintenance
29 C.F.R. § 1910.12(b) defines construction work as work for construction, alteration, and/or repair, including painting and decorating, reconfiguration of space or installation of substantially new equipment.
Construction standards found in 29 C.F.R. pt. 1926. Refurbishing of existing equipment and space = maintenance. Maintenance operations are covered by OSHA standard 29 C.F.R. § 1910
29 C.F.R. § 1910.146 does not apply to construction activities, it does apply to maintenance type operations in confined spaces. Example: relining of a sewer line sleeve which is pushed through a section of the existing system.

## Slide 8: Employer (Risk Managers?) Must:
Evaluate workplace to determine if any spaces are permit-required confined spaces.
Inform employees of any permit-required confined spaces. Post signage at confined spaces as specified by: CFR §1910.146(c)
If employer decides employees will not enter permit-required confined space, it must “take effective measures” to prevent employees from entering.
TAKING EFFECTIVE MEASURES: TOUGHER THAN YOU THINK.

## Slide 9: Non-Permit Confined Space
Non-permit confined space means a confined space that does not contain or, with respect to atmospheric hazards, have the potential to contain any hazard capable of causing death or serious physical harm.

## Slide 10: Permit-Required Confined Space
Permit-required confined space (permit space) means a confined space that has one or more of the following characteristics:
Contains or has a potential to contain a hazardous atmosphere;
Contains a material that has the potential for engulfing an entrant;
Has an internal configuration such that an entrant could be trapped or asphyxiated by inwardly converging walls or by a floor which slopes downward and tapers to a smaller cross- section; or
Contains any other recognized serious safety or health hazard.
Steps example: Large scale HVAC system which required stepping 20 inches above ground to get into restricted opening, resulted in permit required confined space.

## Slide 11: Different Spaces, Different Standards (Thanks Feds)
Confined Space: permit Required, litany of regulations apply (more to come).
Alternate Procedures: don’t have to comply with 29 CFR § 1910.146:
Subsection (d) Confined space evaluation, implement program.
Subsection (e) Create permitting system.
Subsection (f) Fill out confined space entry permit.
Subsection (h) Assign duties of authorized entrants.
Subsection (i) Assign duties of attendants.
Subsection (j) Assign duties of entry supervisors.
Subsection (k) Design Rescue Emergency Services.

## Slide 12: Alternate Entry Procedures v. Permit Required 29 CFR § 1910.146 (c)(5)(i)
An employer may use alternate procedures if employer can demonstrate:
(A) Only hazard posed by the permit space is an actual or potential hazardous atmosphere;
(B) Continuous forced air ventilation alone is sufficient to maintain that permit space safe for entry;
(C) The employer develops monitoring and inspection data that supports the demonstrations required.
(D) If an initial entry of the permit space is necessary to obtain the data required by paragraph (c)(5)(i)(C) of this section, the entry is performed in compliance with paragraphs (d) through (k) of this section;
(E) The determinations and supporting data required by paragraphs (c)(5)(i)(A), (c)(5)(i)(B), and (c)(5)(i)(C) of this section are documented by the employer and are made available to each employee who enters the permit space under the terms of paragraph (c)(5) of this section or to that employee’s authorized representative; and

## Slide 13: Alternate Procedures §1910.146(5)(ii):
(A) Any conditions making it unsafe to remove an entrance cover shall be eliminated before the cover is removed.
(B) When entrance covers are removed, the opening shall be promptly guarded by a railing, temporary cover, or other temporary barrier that will prevent an accidental fall through the opening and that will protect each employee working in the space from foreign objects entering the space.
(C) Before an employee enters the space, the internal atmosphere shall be tested, with a calibrated direct-reading instrument, for oxygen content, for flammable gases and vapors, and for potential toxic air contaminants, in that order. Any employee who enters the space, or that employee’s authorized representative, shall be provided an opportunity to observe the pre-entry testing required by this paragraph.
(D) There may be no hazardous atmosphere within the space whenever any employee is inside the space.
(E) Continuous forced air ventilation shall be used, as follows:
(1) An employee may not enter the space until the forced air ventilation has eliminated any hazardous atmosphere;
(2) The forced air ventilation shall be so directed as to ventilate the immediate areas where an employee is or will be present within the space and shall continue until all employees have left the space;
(3) The air supply for the forced air ventilation shall be from a clean source and may not increase the hazards in the space.

## Slide 14: Alternate Procedures, continued.
(F) The atmosphere within the space shall be periodically tested as necessary to ensure that the continuous forced air ventilation is preventing the accumulation of a hazardous atmosphere. Any employee who enters the space, or that employee’s authorized representative, shall be provided with an opportunity to observe the periodic testing required by this paragraph.
(G) If a hazardous atmosphere is detected during entry:
(1) Each employee shall leave the space immediately;
(2) The space shall be evaluated to determine how the hazardous atmosphere developed; and
(3) Measures shall be implemented to protect employees from the hazardous atmosphere before any subsequent entry takes place.
(H) The employer shall verify that the space is safe for entry and that the pre-entry measures required by paragraph (c)(5)(ii) of this section have been taken, through a written certification that contains the date, the location of the space, and the signature of the person providing the certification. The certification shall be made before entry and shall be made available to each employee entering the space or to that employee’s authorized representative.

## Slide 15: Permit Required
Subsection (d) has 14 requirements.
  Prevent unauthorized entry.
  Identify evaluate all hazards before entry.
  Develop means and procedures for entry (list of requirements to this).
  Provide PPE, testing, communications, ventilation, lighting, barriers/barricades, access equipment (ladders), any other equipment.
  Evaluate safety of space on an ongoing basis.
  Provide at least 1 extra worker outside to monitor for conditions, respond to distress call.
  One can monitor two spaces, but really can’t.
  Designate roles of each person assigned to job.
  Develop implement rescue procedures for each confined space, (tailor procedures).
  Develop implement wrap up procedures.

## Slide 16: Permit Required
Subsection (e) Permit System has 6 requirements:
  Establish permit, naming conditions, procedures, etc.
  Formally authorize entry with supervisor signature.
  Duration of permit needs to be set and adhered to.
  Terminate permit when job completed or new condition arises not identified on permit.
  Retain permits for at least 1 year, review each permit at end of year.

## Slide 17: Permit Required
Subsection (f) entry permit information has 15 conditions.
Subsection (g) Training required for permit procedures and alternate entry procedures.
  Assigned duties established, change in duties requires retraining before implemented.
  Require employees demonstrate proficiency.
  Employer certification of training.

## Slide 18: Permit Required
Subsection (h) duties of entrants 5 conditions.
Subsection (i) duties of attendants 10 conditions.
Subsection (j) duties of entry supervisors 6 conditions.
Subsection (k) Rescue and emergency services 4 epic conditions.

## Slide 19: Employee Participation Required
Employee participation required when formulating a confined space policy. 29 CFR 1910.146 (l):
(1) Employers shall consult with affected employees and their authorized representatives on the development and implementation of all aspects of the permit space program required by paragraph (c) of this section.
(2) Employers shall make available to affected employees and their authorized representatives all information required to be developed by this section.

## Slide 20: Additional resources:
OSHA opinion letters: https://www.osha.gov/laws-regs/interlinking/standards/1910.146
Request consultations with Utah Occupational Safety and Health: https://www.osha.gov/laws-regs/interlinking/standards/1910.146
1910 | Occupational Safety and Health Administration
Look at Appendices!